## Slide 1: Uncertainty Quantification in the Dynamic Analysis of Offshore Structures
HyeongUk Lim
11/21/2019
Mechanics, Uncertainty, and Simulation in Engineering
The University of Texas at Austin

## Slide 2: A Collection of Findings in an Uncertain Grad School Life
HyeongUk Lim
11/21/2019
Mechanics, Uncertainty, and Simulation in Engineering
The University of Texas at Austin

## Slide 3: Contributions
Studied surrogate modeling for offshore design problems using a spectral method: Polynomial Chaos Expansion (PCE)
Developed a distribution-free PCE framework to enhance the traditional spectral method
Proposed a 2-step gradient-based dimension reduction and surrogate modeling for high-dimensional multivariate functions
Validated the proposed methods in offshore dynamics problems for Uncertainty Quantification

## Slide 4: Contributions
Studied an alternative method
Enhanced the traditional method
Proposed a dimension reduction method
Validated proposed methods for Uncertainty Quantification in offshore design

## Slide 5: Uncertainty Quantification in the Dynamic Analysis of Offshore Structures
HyeongUk Lim
11/21/2019
Mechanics, Uncertainty, and Simulation in Engineering
The University of Texas at Austin
Count
Quantity

## Slide 6: Uncertainty Quantification in the Dynamic Analysis of Offshore Structures
HyeongUk Lim
11/21/2019
Mechanics, Uncertainty, and Simulation in Engineering
The University of Texas at Austin

## Slide 7: Why Uncertainty Quantification? And since when?
Image sources: norsar.no (left) ; armscontrol.org (right)
Former President Bill Clinton signing the Comprehensive Nuclear-Test Ban Treaty on September 24, 1996 (CTBTO Photo).

## Slide 8: Why the need for Uncertainty Quantification?
Design verification by computer simulations
But computational models are not scientific theory
Computer-Aided Engineering (CAE)
They are implementations that are mathematical approximations of the underlying scientific theory
Did we build the model right?
 Model Verification
Did we build the right model?
 Model Validation
Did we account for real-world uncertainties?
 Uncertainty Quantification
max impact force?
(Peter Qian, 2017)

## Slide 9: The use of UQ is growing rapidly …
ScienceDirectsearch statistics for articles with
"Uncertainty Quantification" in title, abstract or author-specified keywords
Number of Articles
188
1047
2948
8489
26867
1960-79
1980-90
1991-00
2001-2010
2011-present
(Peter Qian, 2017)
SAE G-11 Probabilistic
Methods Committee (1998)
AIAA Non-Deterministic Approaches
Conference Technical Committee (1999)
SIAM/ASA Journal on Uncertainty
Quantification (2013)
ASME Journal of Verification,
Validation and Uncertainty
Quantification (2016)

## Slide 10: What is Uncertainty Quantification?
Uncertainties in “input” variables are modeled by:
Computation model relates “input” to “response” of interest:
Uncertainty Quantification seeks statistics of “response”:

## Slide 11: Uncertainty Quantification in the Dynamic Analysis of Offshore Structures
HyeongUk Lim
11/21/2019
Mechanics, Uncertainty, and Simulation in Engineering
The University of Texas at Austin

## Slide 12: Why UQ for Offshore Structures?
The ocean surface is irregular in space and time:
Ocean surface can be highly variable, with severe extremes (e.g., hurricane)
Aerial photo of ocean waves
(Fonseca)
(Adcock et al, 2019)
Wave elevation time record

## Slide 13: What happens if we fail in UQ studies?
Hurricane Katrina 2005:
Radius: 24 miles
Max. wave height: 91 ft (28 m)
Severe structural damage:
(NOAA, 2005)
(Gilbert, 2019)
Collapse
Bending
Buckling
30 m

## Slide 14: How do we quantify ‘‘Uncertainty’’?
Computational model, f(x): (e.g., stochastic time series simulator)
Steps:
  (1) Sample input parameter sets
  (2) Propagate to the model
  (3) Seek statistics in the computed output
Quantity of Interest: (e.g., maximum value in time series)
Propagation methods:
  Monte Carlo simulations in f(x)
: maximum

## Slide 15: Uncertainty Quantification in the Dynamic Analysis of Offshore Structures
HyeongUk Lim
11/21/2019
Mechanics, Uncertainty, and Simulation in Engineering
The University of Texas at Austin
(Top)
(Bottom)
Cross-flow riser response
(Lim, Manuel, Low, and Srinil, 2017)
Wave elevation (Lim and Manuel, 2019)
Wood floor response (Lim, Manuel, Persson, and Andersen, 2019)
Floating structure response (surge) (Lim, Manuel, and Low, 2018)

## Slide 16: What I have worked on:
Approximation
Integration
Integration

## Slide 17: But we face the ‘‘curse of dimensionality’’
Model order reduction
Dimension | 5 points per dimension | 1 min per run
1 | 5 | 5 min
2 | 52= 25 | 25 min
3 | 53= 125 | 2 hours
4 | 54= 625 | 10 hours
5 | 55= 3125 | 2 days
… | … | …
10 | 510= 9765625 | 19 years
Sampling strategy
Dimension reduction

## Slide 18: Surrogate Model can help
1 min per single run
5 min
25 min
2 hours
10 hours
2 days
…
19 years
No. of runs
5
25
125
625
3125
…
9765625
10 μs per single run
50 μs
250 μs
1.25 ms
6.25 ms
31.25 ms
…
2 mins

## Slide 19: Surrogate Model
A surrogate model approximates a computational model by using:
  a small number of the “truth” model runs in construction;
  assumed characteristics.
truth
surrogate
minutes or hours per run
vs.
seconds per 106 runs

## Slide 20: To name just a few surrogate model approaches:
Polynomial Chaos Expansion
Gaussian Process
Deep Learning
Generative Adversarial Networks
Support Vector Machine
First Order Reliability Method
Second Order Reliability Method
Subset Simulation
Neural Network
Low Rank Approximation
Convolutional Neural Network
Sliced Inverse Regression
Sliced Average Variance Estimate
Principal Hessian Direction
Active Subspace
Bayesian
Wiener Path Integration
Environmental Contour Method
Maximum Entropy Distribution
Machine Learning
Karhunen-Loeve Expansion
Polynomial Dimension Decomposition

## Slide 21: Spectral Approach: Polynomial Chaos Expansion
Use a finite-degree polynomial series expansion to approximate an unknown function.
stochastic
output
basis polynomials
in input variables
stochastic
input
coordinates
: basis functions
arrow length: coordinate
:

## Slide 22: How to use PCE?
Truth model:
PCE model:
  Choose basis functions: Hermite polynomials
  Variable transformation: [easily generalizable]
Expand:

## Slide 23: PCE Coefficient Estimation
Spectral projection:
Linear regression:
Coefficient estimation requires some computational runs with the “truth” model.

## Slide 24: Contributions
Studied surrogate modeling for offshore design problems using a spectral method: Polynomial Chaos Expansion (PCE)
Developed a distribution-free PCE framework to enhance the traditional spectral method
Proposed a 2-step gradient-based dimension reduction and surrogate modeling for high-dimensional multivariate functions
Validated the proposed methods in offshore dynamics problems for Uncertainty Quantification
Example: Fatigue damage in a marine riser due to vortex-induced vibration

## Slide 25: Why we care?
Risers become more vulnerable to VIV as oil and gas development moves to deeper water
VIV prediction is notoriously difficult; current practice relies on very large safety factors
TRACS (tensioned riser assessment for continued service) JIP (joint industry project)
(J. Kim Vandiver's MIT research team)
marine riser
vortex-induced vibration

## Slide 26: UQ Framework
(Top)
(Bottom)
V: uniform current velocity (m/s)
D: riser diameter (m)
L: riser length (m)
Input
Output
Partial Differential Equation
Fatigue damage
(normalized)

## Slide 27: Prediction by different PCE models
PCE surrogate modeling appears to be quite accurate
Exceedance probabilities are within 99% confidence intervals of MCS.

## Slide 28: Sometimes PCE doesn’t do a very good job
When f(x) is complex (beyond description by polynomials):
  e.g., rational functions
What causes complications?
  Underlying distributions AND nonlinear transformations
truth model in X domain
truth model in Q domain
surrogate in Q domain

## Slide 29: Non-Parametric Polynomials
Univariate Gram-Schmidt Polynomials:
Multivariate Gram-Schmidt Polynomials for Dependent Variables:
generalization
We can use empirical mp.

## Slide 30: Contributions
Studied surrogate modeling for offshore design problems using a spectral method: Polynomial Chaos Expansion (PCE)
Developed a distribution-free PCE framework to enhance the traditional spectral method
Proposed a 2-step gradient-based dimension reduction and surrogate modeling for high-dimensional multivariate functions
Validated the proposed methods in offshore dynamics problems for Uncertainty Quantification
Revisit Example: Fatigue damage in a marine riser due to vortex-induced vibration

## Slide 31: Distribution-free PCE: Arbitrary PCE (APCE)
APCE show good estimates of mean and variance of QoI (Quantity of Interest): Fatigue Damage (normalized).
APCE does not assume any distribution for inputs, while traditional (parametric) HPCE utilizes jpdf of X and iso-probabilistic mapping, T.
 | Truth | APCE | HPCE
mean | 6.797 | 6.806 | 6.814
var | 87.905 | 87.719 | 93.548
m= 5

## Slide 32: Can PCE work for high-dimensional problems?
Extremely difficult
How to deal with this?
  (1) Select important variables or
  (2) Reduce problem dimension (by transforming original coordinates to “active” ones).

## Slide 33: Given:
Trying different linear combinations of X for 1-d manifold
GOAL:
to find appropriate W
1-d quadratic function approximately

## Slide 34: Dimension Reduction
uses gradient to find W:
Dimension Reduction Using Gradient

## Slide 35: Define a Subset: ‘‘Active Subspace’’
The function, its gradient vector, and a pdf:
The covariance matrix and its eigendecomposition:
Eigenvalues describe the function’s hidden structure (with associated eigenvectors):
Interpretation:
how much f changes with respect to each direction in a mean-squared sense.

## Slide 36: Interpretation: Coordinate Rotation
Rotate
Direction
of variability
Direction
of flat

## Slide 37: Summary
Input
Output
subset
Dimension is too large for
surrogate modeling
Dimension is moderate
‘‘Active Subspace’’

## Slide 38: Gradient Calculation must still address the ‘‘curse of dimensionality’’
Model-order reduction first; search for active subspace next
Input
Output
subset
‘‘Active Subspace’’
Reduced
Input

## Slide 39: Contributions
Studied surrogate modeling for offshore design problems using a spectral method: Polynomial Chaos Expansion (PCE)
Developed a distribution-free PCE framework to enhance the traditional spectral method
Proposed a 2-step gradient-based dimension reduction and surrogate modeling for high-dimensional multivariate functions
Validated the proposed methods in offshore dynamics problems for Uncertainty Quantification

## Slide 40: Stochastic Time Series Simulator for Long-term Response Prediction
Wave process
simulations
Response simulation
T-minute
extreme response
Short-term
response distribution
Short-term
Long-term
Long-term
response distribution
Environmental
variables
Joint PDF
of environment
Integrate
Hundreds of harmonics are necessary
A few important harmonics for Z

## Slide 41: Model Order Reduction in Fourier Series

## Slide 42: Gradient Approximation
Uniform
Standard Normal
Response
2+2r function calls
One function call

## Slide 43: Establish Gradient Vectors
1st
2nd
3rd
…
Nth
C= GGT/N
Total function calls: N(1 + 2 + 2r)
C= WΛWT

## Slide 44: Surrogate Modeling in Reduced Dimension Space
Model order reduction
Dimension reduction
Surrogate modeling

## Slide 45: Contributions
Studied surrogate modeling for offshore design problems using a spectral method: Polynomial Chaos Expansion (PCE)
Developed a distribution-free PCE framework to enhance the traditional spectral method
Proposed a 2-step gradient-based dimension reduction and surrogate modeling for high-dimensional multivariate functions
Validated proposed methods in offshore dynamics problems for Uncertainty Quantification
Examples: Long-Term Extreme Response Prediction in Offshore Dynamics

## Slide 46: North Sea
A jpdf was proposed by Haver and Nyhus (1986).
Wave scatter diagram at North Sea
Source: Norwegian Meteorological Institute
North Sea
Barents Sea

## Slide 47: Model Exploration: Max Wave Elevation
North Sea
Barents Sea
Eureka
Sites
Bretschneider Pierson-Moskowitz JONSWAP
Wave Spectra
Wave elevation Floating structure Energy extractor
Short-Term Interest
Hs= 12.6 (m) Tp= 15.0 (s)
Hs
Tp
Red circles: P[Hs>h]>10-4

## Slide 48: Model Order Reduction: Max Wave Elevation
Nω= 15
Hs= 12.6 (m) Tp= 15.0 (s)
North Sea
Barents Sea
Eureka
Sites
Bretschneider Pierson-Moskowitz JONSWAP
Wave Spectra
Wave elevation Floating structure Energy extractor
Short-Term Interest
Nω= 20
Nω= 25
Nω= 30
Nω= 35
Nω= 40
Nω= 45
Nω= 50

## Slide 49: Dimension Reduction: Max Wave Elevation
North Sea
Barents Sea
Eureka
Sites
Bretschneider Pierson-Moskowitz JONSWAP
Wave Spectra
Wave elevation Floating structure Energy extractor
Short-Term Interest

## Slide 50: Extreme Response of SDOF System
Hs
Tp
m = 70.36 (kg); k = 10 (N/m);
c = 2 x 0.01 x sqrt(k x m); wn= 0.38 rad/s = 0.06 Hz= 16.7 (sec)
Larger z values occur for Tp ranges around the natural period
Higher Hs doesn’t necessarily produce higher z
Red circles: P[Hs>h]>10-4
Hs= 12.6 (m) Tp= 15.0 (s)
North Sea
Barents Sea
Eureka
Sites
Bretschneider Pierson-Moskowitz JONSWAP
Wave Spectra
Wave elevation Floating structure Energy extractor
Short-Term Interest

## Slide 51: Model Order Reduction: Extreme Response of SDOF System
Nω= 10
Hs= 12.6 (m) Tp= 15.0 (s)
Nω= 15
Nω= 20
Nω= 25
Nω= 30
Nω= 35
North Sea
Barents Sea
Eureka
Sites
Bretschneider Pierson-Moskowitz JONSWAP
Wave Spectra
Wave elevation Floating structure Energy extractor
Short-Term Interest

## Slide 52: Dimension Reduction: Extreme Response of SDOF
North Sea
Barents Sea
Eureka
Sites
Bretschneider Pierson-Moskowitz JONSWAP
Wave Spectra
Wave elevation Floating structure Energy extractor
Short-Term Interest

## Slide 53: Contributions
Studied surrogate modeling for offshore design problems using a spectral method: Polynomial Chaos Expansion (PCE)
Developed a distribution-free PCE framework to enhance the traditional spectral method
Proposed a 2-step gradient-based dimension reduction and surrogate modeling for high-dimensional multivariate functions
Validated the proposed methods in offshore dynamics problems for Uncertainty Quantification

## Slide 54: Thank you for your attention
“When nothing is sure, everything is possible.” – Margaret Drabble
Topics I delivered:
Uncertainty Quantification
Polynomial Chaos Expansion
Dimension Reduction Using Gradients
Applied to offshore dynamics:
Fatigue Damage in a Marine Riser Due to VIV
Long-term Extreme Wave Elevation Prediction
Long-term Extreme Structural Response Prediction
Related questions:
Have I ever compared different surrogate methods?
Have I ever applied the methods to MDOF systems?
Can the proposed method be applied to more complex structures?
Have I compared different sites of interest?
Which variable is most important?
How to validate the results when there is no observatory data to compare?